## Slide 1: An augmented reality debugging system for robot swarms
Alistair Jewers
Supervisor – Alan Millard

## Slide 2: Swarm Robotics
Relatively new area of research
Specific kind of multi-robot system
Large number of relatively simple robots working together
Decentralised control - local information only
Originated from swarm intelligence and the study of social insects
Unique challenges in development and debugging
  Large numbers of robots
  No central information point
introduction
Ducatelle F., Di Caro G. A., Pinciroli C., Mondada F. and Gambardella L. M., Communication assisted navigation in robotic swarms: self-organization and cooperation. Proceedings of the IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS), San Francisco, USA, September 25-30, 2011

## Slide 3: Robotics debugging tools
Robotic systems differ from traditional software
  Real world environment
  Greater numbers of inputs
  Wider ranges of possible input values
More difficult to isolate issues, reproduce faults, and fix bugs
Problem amplified when working with multi-robot systems such as swarms
Traditional text-based debugging tools not always sufficient
New tools needed to retrieve and display system information in real time
introduction

## Slide 4: Augmented reality
AR presents new opportunities for robotics debugging
An augmented combines a real space and a digital one
Can be inherently understood by both humans and robots
Broadens the human-robot communication channel
Humans can parse physical spaces much faster than text or numbers
introduction
Microsoft HoloLens. © Microsoft corporation. https://www.microsoft.com/microsoft-hololens/en-us/hardware

## Slide 5: Project concept
Aims to create a software tool for monitoring and debugging robot swarms
Will incorporate a live video feed of the robots
Connect to the robots wirelessly and retrieve internal data
Augment the video feed with graphical representations of the retrieved data
introduction
ROBOT1
STATE: IDLE
Raw video of robots
Robots transmit data
Video augmented with data representations

## Slide 6: Hardware
Practical work carried out at the York Robotics Laboratory, on Heslington East
Initial target robot platform is the ‘e-puck’ robot
  Robotics education and research platform
  Widely used in multi-robot and swarm research
  Configured with a Linux extension board and WiFi adapter
Machine vision camera
  Positioned directly above robot arena
Robots tracked using the ‘ARuCo’ tag detection system
BACKGROUND

## Slide 7: Hardware
BACKGROUND
An e-puck robot with the Linux extension board attached.

## Slide 8: Hardware
BACKGROUND
Left: Four printed ARuCo tag markers. Right: An e-puck robot with a laser cut ARuCo marker header attached.

## Slide 9: Hardware
BACKGROUND
Machine vision camera used for tracking.
Three e-puck robots in the robot arena, beneath the tracking camera.

## Slide 10: System Architecture
Robots communicate data over WiFi
Camera sends images via Ethernet
Application formed of a server portion and a UI
Design

## Slide 11: software Architecture
Model View Controller architecture
Model stores data about the robot
View displays the data through the UI and augmented video
Controller handles receiving data, updating the model, reading the camera
Application is threaded to improve performance
Modular design to improve future extensibility
Design

## Slide 12: UI design
3 main panels, Visualiser, Robot List and Detail
UI created using the popular Qt GUI framework
Image processing managed using OpenCV
Design

## Slide 13: UI design
Design

## Slide 14: Application
Implemented in C++
All core aspects of the application have been implemented
Robot tracking and video feed augmentation
Progress
Tracking the position and orientation of three robots.
Displaying the tracked path history of a moving robot.

## Slide 15: Application
Several data types implemented in both data model and UI
Progress
Here the IR data for robot 0 is being examined. This includes a graphical representation in the visualiser and details of the raw data in the details panel.

## Slide 16: Application
Several data types implemented in both data model and UI
Progress
Here the states and state transition history of one of the robots is examined in the details panel.
This tab shows the custom data reported by one of the robots. The application supports an unlimited number of custom key-value pairs, defined on the robot side.

## Slide 17: Robot Code
Networking code
Accessed through single-class API
Implemented in C++
Portable
Progress

## Slide 18: Remaining Features
[??]
Future Work

## Slide 19: Testing and Evaluation Strategy
Formal testing work yet to be completed
  Manual user interface testing
  Unit testing of data model
  Verification testing of the system as a whole
Evaluation through observed user trials
  Users will be asked to monitor a swarm and attempt to solve a deliberate bug
  Followed by a questionnaire about the system’s usability and design
Future Work

## Slide 20: Potential future Development
  This system could be developed into a full swarm robotics research platform
    Record and export data from swarm robotics experiments
    Perform data processing and macro-level analysis in real time
    Export video of experiment runs
    Allow for bi-directional communication with the robots to send instructions
  Extend to more robot platforms
    The robot side code should be relatively easy to port to other robots
    Implement support for Bluetooth as well as WiFi for data transfer
  Ported to a more comprehensive AR platform
    Microsoft Holo-lens integration would allow for more immersive human-robot interaction
Future Work

## Slide 21
  Developed in order to tackle issues with debugging swarm robotics systems in real time.
  Designed with a focus on modularity, extensibility, with an MVC architecture in mind.
  Implementation stage is almost complete, with testing and evaluation to begin soon.
  Potential to be developed into a full Swarm Robotics research platform in the future.
Conclusion

## Slide 22: Thank you for Listening
Feel free to ask any questions
Conclusion